## Slide 1
Sleep EEG Research
Study Dataset Overview
Control
8 subjects
Dup15q
11 subjects
Rett
8 subjects
UCLA Collaboration • Nihon Kohden EEG System • EEGLAB/MATLAB Pipeline

## Slide 2
Study Design
Three subject groups compared via overnight sleep EEG
Control
8 subjects
Typically-developing
IDs: 3912633, 4068015,
4137123, 4329285,
4757853, 5141475,
5360954, 5409426
Raw NKT data
Dup15q
11 subjects
Dup15q syndrome
IDs: 4546621, 4574335,
4646135, 4672497,
4745551, 4939552,
4959323, 4969700,
4981316, 5158834, 5426282
Raw NKT data
Rett
8 subjects
Rett syndrome
EA1720U (2-night merge)
EEG 030, 034, 036,
038, 041, 043, 044
(7-hr clean recordings)
Processed ✓

## Slide 3
Processing Pipeline
MATLAB / EEGLAB — 3-stage workflow
Raw EDF
Nihon Kohden
▶
Stage 1 | Import
⚙ config_import.mat
• EDF → EEGLAB .set/.fdt
• Standardise channel labels
• Output: *_import.set
▶
Stage 2 | Preprocessing
⚙ config_prep.mat
• Assign channel locations (10-20)
• Artifact rejection & cleaning
• ICA decomposition
• ICLabel classification
• Output: *_prep.set
▶
Stage 3 | Spectral Analysis
⚙ CONFIG.mat
• Epoch-based power spectra
• 5 frequency bands computed
• Topomaps + TF spectrograms
• Output: Report directory
Report
Directory
.xlsx
.png
topo-
maps
.png
TF plots
▶

## Slide 4
Channels & Frequency Bands
International 10-20 Channel Montage (22 EEG)
Frontal
Fp1, Fp2, Fpz, F3, F4, F7, F8, Fz
Central
C3, C4, Cz
Temporal
T1, T2, T3, T4, T5, T6
Parietal
P3, P4, Pz
Occipital
O1, O2
Reference
A1, A2
ECG
ECGL, ECGR
EMG
EMG1, EMG2
EOG
LOC, ROC
Frequency Bands Analyzed
Delta
0.5 – 4 Hz
Dominant in deep sleep
Theta
4 – 8 Hz
Light sleep / drowsiness
Alpha
8 – 13 Hz
Relaxed wakefulness
Beta
13 – 30 Hz
Active cognition
Gamma
30 – 50 Hz
High-frequency processing

## Slide 5
Analysis Outputs per Subject
Each processed recording produces a Report directory with the following files
ICLabel.png
ICA Component Classification
Grid of scalp topoplots — one per ICA component — labeled Brain / Eye / Other with confidence %. Used to reject non-brain artifacts.
power_{band}.png
Absolute Power Topomaps
Scalp heatmaps showing absolute spectral power (μV²) for each of 5 bands. Color: blue (low) → red (high). One file per band.
rpower_{band}.png
Relative Power Topomaps
Normalized 0–1 topomaps showing what fraction of total power each band contributes. Delta typically dominates (0.4–0.9) in sleep.
tfplot_{channel}.png
Time-Frequency Spectrograms
Per-channel plots: time (sec) on x-axis, frequency (Hz, up to 50) on y-axis. Color = log power. Shows sleep stage shifts over time.
Result_*.xlsx
Power Values Spreadsheet
Excel table of computed spectral power across all bands and channels. Primary quantitative output for statistical comparison between groups.

## Slide 6
Current Dataset Status
Rett — PROCESSED ✓
✓ EA1720U (2-night merged)
✓ EEG 030 — 7hr clean
✓ EEG 034 — 7hr clean
✓ EEG 036 — 7hr clean
✓ EEG 038 — 7hr clean
✓ EEG 041 — 7hr clean
✓ EEG 043 — 7hr clean
✓ EEG 044 — 7hr clean
Control & Dup15q — RAW DATA
Control (8 subjects)
○ 3912633
○ 4068015
○ 4137123
○ 4329285
○ 4757853
○ 5141475
○ 5360954
○ 5409426
Dup15q (11 subjects) — NKT format
4546621 · 4574335 · 4646135 · 4672497 · 4745551 · 4939552 · 4959323 · 4969700 · 4981316 · 5158834 · 5426282
Next step: Run MATLAB pipeline on Control & Dup15q groups to enable cross-group comparison

## Slide 7
resteeg-master
Automated Analysis of Resting-State EEG for Clinicians
Purpose
▸ Single MATLAB function call processes raw EEG through the full pipeline
▸ Skips already-completed stages automatically (import / preproc)
▸ All parameters are passed via a CONFIG struct — reproducible & auditable
▸ Generates topomaps, TF spectrograms, and Excel power tables automatically
▸ Batch-processes multiple subjects in a loop from one config file
File Structure
resteeg-master/
├─ resteeg.m
│ ← main function (entry)
├─ tutorial_resteeg_vidya.m
│ ← our config & run script
├─ functions/
│ prep_import.m
│ prep_proc.m
│ gen_report_materials.m
│ export_feature.m
│ export_excel.m
├─ chanlocs/
│ chanlocs_nihonkohden.mat

## Slide 8
tutorial_resteeg_vidya.m — Entry Point
How to run the pipeline on new subjects
1
Setup Paths
uigetdir() prompts for EEGLAB folder, resteeg folder.
Sets chanlocs path → chanlocs_nihonkohden.mat
▶
2
Select Files
uigetfile() to pick one or more .set files.
Supports multi-select for batch processing.
▶
3
Configure
Set CONFIG struct:
filter: HP 1 Hz, LP 55 Hz | reref: average
ASR cutoff: 20 | ICLabel threshold: 0.5
Time window: [1, 21591] sec
▶
4
Run Loop
for each file → CONFIG.filename = file
CONFIG = resteeg(CONFIG)
Failed files caught and logged.
▶
5
Export to Excel
uigetfile_n_dir selects report folders.
export_feature() → export_excel()
Outputs: Result_Baseline_Power.xlsx
CONFIG = resteeg(CONFIG); % called once per subject inside the for-loop

## Slide 9
resteeg.m — Main Function
Smart caching: each stage checks for existing output before re-running
① Import
prep_import(CONFIG)
EDF/BDF/SET → EEGLAB format
Channel removal + location assign
Time window selection
▼
② Preprocessing
prep_proc(EEG, CONFIG)
Filter → Bad ch. removal → Reref
CleanLine (60/120 Hz)
ASR → ICA + ICLabel rejection
▼
③ Power Analysis
power_analysis(EEG, CONFIG)
PSD via spectopo() → 5 bands
Absolute + relative power
Frontal alpha asymmetry (F3/F4, F7/F8)
▼
④ TF Analysis
time_freq_analysis(EEG, CONFIG)
Hann-windowed STFT
Spectrogram 1–50 Hz, log power
Saves tfplot_{channel}.png per channel
▼
⑤ Generate Report
gen_report_materials(EEG, CONFIG)
Saves CONFIG.mat
10× topomap PNGs (power + rpower)
Optional: gen_report()
Smart Skip / Cache
*_import.set exists?
FORCE_RUN_IMPORT = 0
→ Skip import, load from disk
*_prep.set exists?
FORCE_RUN_PREPROC = 0
→ Skip preprocessing, load from disk
SAVESET = 1 → writes .set files after each stage
double_precision = 0 → use float (faster)
EXPORT_REPORT = 0 → skip PDF report

## Slide 10
Stage 1 & 2 Deep Dive — Import & Preprocessing
prep_import.m — Stage 1: Import
import_data()
Loads EDF/BDF via pop_biosig()
or .set via pop_loadset()
Stores nbchan, srate, xmax in rawinfo
▼
remove_channel()
Removes user-specified non-EEG
channels via pop_select()
(e.g. EMG, ECG, DC channels)
▼
import_chanlocs()
Loads chanlocs_nihonkohden.mat
Assigns 3D electrode positions
Fallback: template lookup
▼
select_time()
Trims to CONFIG.time_window
[1, 21591] sec for our data
(~6 hours overnight)
prep_proc.m — Stage 2: Preprocessing
Basic
filter_data()
HP: 1 Hz FIR | LP: 55 Hz FIR
pop_eegfiltnew()
Basic
remove_badchan()
pop_rejchan (±3 SD spectral)
clean_flatlines + clean_channels
(flatline 5s, corr 0.6, noise 4 SD)
Basic
interp_badchan()
Spherical interpolation
of removed bad channels
pop_interp()
Basic
reref_data()
Average reference
pop_reref(EEG, [])
Adv.
remove_linenoise()
CleanLine plugin: 60 + 120 Hz
pop_cleanline()
Adv.
asr_autoclean()
Artifact Subspace Reconstruction
stdcutoff = 20
clean_asr()
Adv.
ica_autoclean()
runica ICA → ICLabel classifier
Reject: Muscle/Eye/Heart/Line/Chan
threshold = 0.5

## Slide 11
Stage 3 Deep Dive — Power & Time-Frequency Analysis
power_analysis() — resteeg.m
[spectra, freqs] = spectopo(EEG.data, 0, EEG.srate);
power_delta = mean(10.^(spectra(:, freqs>=1 & freqs<4)/10), 2);
power_alpha = mean(10.^(spectra(:, freqs>=8 & freqs<13)/10), 2);
...
total = sum([delta, theta, alpha, beta, gamma], 2);
rpower_delta = power_delta ./ total;
PSD method
spectopo() — EEGLAB's FFT-based power spectral density
5 bands computed
Delta 1–4 | Theta 4–8 | Alpha 8–13 | Beta 13–30 | Gamma 30–50 Hz
Relative power
Each band / sum of all 5 bands (0–1 normalized)
Alpha asymmetry
(F3−F4)/(F3+F4) and (F7−F8)/(F7+F8) — frontal lateralization index
time_freq_analysis() — resteeg.m
window = hann(window_len * EEG.srate); % 5-sec Hann
noverlap = floor(length(window) / 2);
nfft = max(256, 2.^ceil(log2(length(window))));
[s, f, t] = spectrogram(EEG.data(ch,:), window,
noverlap, nfft, EEG.srate);
log_power = log(abs(s(freq_range,:)).^2);
Window
5-second Hann window (configurable via timefreq_window_len)
Overlap
50% overlap (floor(window/2) samples)
Freq. range
1–50 Hz displayed | NFFT = next power of 2 ≥ window length
Color scale
log power, clipped to [0.25th percentile, max] | jet colormap
Channels
CONFIG.report.timefreq_plot_chan = {T3, T4, P3, P4} in our setup
Output
tfplot_{channel}.png saved to report directory